# HITACH BASIC MASTER LEVEL3 / MB-S1
# VFO Interface for MP-1802 / MP-1870
Designed by Sasaji 2022 Rev. 0.1.2
This is an interface board connecting between a floppy disk drive and MP-1802 / MP-1870, the FD interface card on a PC.
You can use this on HITACHI BASIC MASTER LEVEL3 / Mark II / Mark5 and MB-S1.
Connecting to the GOTEK floppy emulator
# Preparing
To use this board, you need to prepare the following :
- The FD interface card MP-1802 or MP-1870 must be present on the computer.
- FDD Emulator (GOTEK)
- Power: +5V, 1A (A switching AC adapter etc.)
- Cable to connect with the computer: 50-pin Amphenol <-> 50-pin IDC connector (2.54mm pitch x 2 rows)
- Cable to connect with FDD: 34-pin IDC connector cable (2.54mm pitch x 2 rows)

# Role of each part

Power input +5V
DC Barrel Jack
(Center plus)
Power input +5V
EI connector
(+5V,Gnd,Gnd,N/C)
Connect to FDD
Connect to PC
Power output +5V
Connect to FDD
(Linked with power switch)
Power switch
Jumper
Jumper

+
-

# Jumper pins

READY:
Select which the READY signal from the FDD is coming from.
pin34 or pin6
Short pins vertically.

HEAD LOAD:
Select which the HEAD LOAD signal from the computer is coming from.
pin4 or pin2
Short pins vertically.

SELECT:
Selects the behavior of the DRIVE SELECT signal.
- MOT(Short to 1-2)：Connect the signal while the MOTOR signal is ON.
- PUR(Short to 2-3)：Always connect the signal.
# Pinout of the connector
[Attention] The direction of silk printing is reversed. Correctly, the notch is on the upper side (pin 1 side).

### When making your own 50-pin cable
There is a protrusion near pin 26 on the MP-1802/MP-1870 side, so bend this part on the cable side so that it does not hit the protrusion.

# Precautions for use
- Connect only one of the power input J5 (DC jack) and J6 (EI connector).
- Pin 4 (+12V line) of J6 is not connected to anything. When using an FDD that requires +12V, connect the power connector without going through this board.
- If the physical FDD pull-up resistance value is low, drive select may not function properly. In this case, see “About optional functions” section.
- This board is a prototype. Please note that we do not consider the noise generated during use or deterioration over time.
## No Warranty
　We are not responsible for any damage caused by this board.
　Use this board at your own risk.
## Web Site
GitHub(https://github.com/bml3mk5/MP1802Gotek)

Sasaji (sasaji@s-sasaji.ddo.jp)
http://s-sasaji.ddo.jp/bml3mk5/
(Twitter: https://twitter.com/bml3mk5)